CSCI 4830 Semester Project
Analyzing and Comparing Locking Mechanisms
in Varying Systems
By: Stefan Knott

---
Overview
- When and why to use different locking mechanisms across varying levels of contention, CPU set size, and thread pool size
- Motivation: interests in runtime efficiency and concurrency on small scale systems.

---
Implementation
- C/BASH
- Pthread libraries (mux, sem, spin)
- TTASB code implementation with max backoff of 250 miliseconds

---
Implementation Cont'd
- Contention control
- Enter the CS
  - 250 increments
  - O(1) runtime complexity
- Lock delay short

---
Presumptions entering Testing
- Mutex and semaphore seem to be common choices among programmers (lots of well documented libraries, CSCI 3753).
- Spin locks are efficient when lock wait time is short and when we have many processors (pg. 141 Herlihy & Shavit)

---
Testing
- Core set sizes: 2, 4, 8
- Thread pool sizes: 8, 15, 30
- High contention level causes ~40x more contention than low level
- Measuring: Runtime, CPU usage, context switches

---
Results
- Low contention runtime << high contention runtime
- Results separated into “Stressed” and “Relaxed” Systems
- Stressed – CPU set size level <= thread pool size level. Typically low # CPUs needed
- Relaxed – CPU set size level > thread pool size level. Typically high # CPUs needed

---
Low Contention Results
- Use mutex as it's runtime is always less than or equal to the runtime offered by other mechanisms.
  - When system was highly relaxed (high core, low thread pool size) runtime of MUX and SPIN/TTASB equal
- Runtime range for all locks: 0.00-0.02s
  - If this runtime wait difference of 0.02 is negligible – look to CPU usage.
- TTASB consistently uses less CPU power
  - 4x less than MUX in high core low thread case

---
Very Stressed (low core, high con)

---
Stressed (med core, high con)

---
Relaxed (high core, high con)

---
Conculsions
- If system is stressed (lots of work to do on few cores, commonly thread pool size >= core set size) – use MUX or SEM
- If the system is relaxed (some work to do on lots of cores, commonly core set size > thread pool size) – use SPIN
- Side note: if voluntary context switching is expensive use SPIN as it causes nearly 500x less voluntary switches than MUX/SEM. 2X Less involuntary switches as well

---
Remaining thoughts
- Could be beneficial to implement a dynamic system which would change from using spin locks to mutexs or semaphores based on changing stress levels.
- Thanks for listening